## Slide 2: DSEAR and RGP in a novel nuclear application
Keith A Johnson CEng FIChemE,
Gareth Davies, Matthew Webber, Jeff Tattersall
Notes: I’m Keith Johnson
I’m a chemical engineer in the Process Engineering Capability of Sellafield Ltd.
My colleagues: Gareth Davies, Matt Webber and Jeff Tattersall and I wrote this paper based on our work to provide a robust DSEAR case using established practices on a novel situation. It was a facility undergoing high hazard reduction activities.
For commercial reasons I cannot share too much about the plant itself.
What we wanted to do was to avoid reinventing the wheel, hence the question whether Relevant Good Practices from other sectors and the discussion are transferable to this novel situation.

## Slide 3: DSEAR and RGP – The Idyllic Illusion
Notes: I couldn’t resist adding this slide, I call it the Idyllic Illusion
Why?
First, just as an icebreaker!!
Second, as an allegoric introduction that we all like to see the idyllic scene but fail to look beneath the surface and see what we do not want to see before it blows up in our faces.

## Slide 4: DSEAR and RGP - Introduction
High Hazard Reduction Activities
Hydrogen hazard
Engineering Judgement – Hazard! What hazard?
How to underpin the judgement?
Use Relevant Good Practices – (don’t reinvent the wheel)
Satisfies regulator assessment criteria
Avoid confirmation bias
Notes: This is about managing a hydrogen hazard on a nuclear facility undergoing high hazard reduction activities.
And demonstrating compliance with the Dangerous Substances and Explosive Atmospheres Regulations 2002. (DSEAR 2002).
Our initial chemical engineering judgement was pretty much:
Hazard! What hazard?
Because, on face value the residual risk to the operators appears to be negligible.
But the challenge became how to underpin that judgement with sufficient evidence to meet the regulator’s assessment criteria.
So as not to reinvent the wheel could it be done using common relevant good practice (RGP) methodologies from other sectors but transfer them to the novel situation of high hazard reduction operations. What we also needed to avoid confirmation bias?

## Slide 5: DSEAR and RGP – What is RGP (1)
Face value – obvious – isn’t it?
Generic Term
Regulator specific expectation
  standards for controlling risk which they have judged and recognised as satisfying the law when applied to a particular relevant case.
Duty holder responsibility to demonstrate RGP
Notes: First a word about RGP.
On face value RGP is obvious. Isn’t it?
It’s a generic term for common place practices and methodologies to assess, control and manage hazards and their risks.
However, the regulators, both the Office of Nuclear Regulation (ONR) and the Health and Safety Executive (HSE) have their own definition.
RGP to them are those standards for controlling risk which they have judged and recognised as satisfying the law when applied to a particular relevant case.
ONR expands RGP in terms of As Low as Reasonably Practicable (ALARP) in its Technical Assessment Guide 005
Bottom line is that the responsibility remains with the dutyholder to identify and demonstrate that the relevant practices and methodologies used represent RGP to the satisfaction of the Regulator.

## Slide 6: DSEAR and RGP – What is RGP (2)
ONR Hierarchical approach?
Guidance within Approved Codes of Practice (eg DSEAR ACOP L138 2015).
ONR guidance
  Safety Assessment Principles
  Technical Assessment Guides
  Technical Inspection Guides
Notes: The ONR specify a hierarchy of sources of RGP, which includes:
Guidance within Approved Codes of Practice; such as the DSEAR ACOP L138.
ONR’s own guidance including their Safety Assessment Principles, Technical Assessment Guides and Technical Inspection Guides.

## Slide 7: DSEAR and RGP – What is RGP (3)
ONR Hierarchical approach?
Standards
  British Standards Institution
  International Electrotechnical Commission.
Industrial sector guidance eg Energy Institute.
Well defined and established standard practice
Notes: Standards produced by standards making organisations, this includes:
  British Standards Institution.
  International Electrotechnical Commission.
Guidance agreed by a body representing an industrial sector such as the Energy Institute.
Well defined and established standard practice adopted by an industrial or operational sector.

## Slide 8: DSEAR and RGP – Underpinning background
“Satisfies regulator assessment criteria”
Two aspects:
Regulatory Framework
Tolerability of Risk for nuclear sector
Kletz:
  few companies would get a clean bill of health if looked under the regulatory scrutiny to which the UK nuclear industry is subject.
Notes: I previously said the underpinning must satisfy regulatory assessment criteria.
There are two aspects to this that are germane to any discussion of achieving DSEAR compliance and the use of RGP on a nuclear licensed site:
the first is the regulatory framework.
the second is the tolerability of risk within the nuclear industry.
I am going to explore each of these to provide context to the discussion
Before I do, I am minded of Trevor Kletz had to say about the UK regulation of the nuclear industry: few companies would get a clean bill of health if looked under the regulatory scrutiny to which the UK nuclear industry is subject.

## Slide 9: DSEAR and RGP – Regulatory Framework (1)
Regulator - Office of Nuclear Regulation (ONR)
ONR
  Formed 2013 - Energy Act
  Regulator originally HSE through NII
Health and Safety at Work Act
Nuclear Installations Act 1965
  Licensing Regime
Notes: The Office of Nuclear Regulation, the ONR, is the independent statutory regulator, for the nuclear industry. It came into being in 2013 through the 2013 Energy Act.
Before then the Regulator was the HSE, principally through the NII, the Nuclear Installations Inspectorate (NII). The HSE is still the regulator for the majority of UK industry and operates through a mixture of notification and licensing.
We all have to meet the requirements of the Health and Safety at Work Act and the relevant secondary regulations.
The nuclear industry in addition to HASAWA must comply with the 1965 Nuclear Installations Act. This requires a licensing regime. A nuclear licensed site have a specific set of Site License Conditions.

## Slide 10: DSEAR and RGP – Regulatory Framework (2)
Regulator - Office of Nuclear Regulation (ONR)
Six Powers under licence
    Consent
    Approval
    Direction
    Agreement
    Notification
    Specification .
Notes: The ONR have a Licence Condition Handbook, which the standard conditions.
These licence conditions confer six specific powers to the ONR for the control of the licensee’s activities:
Consent
Approval
Direction
Agreement
Notification
Specification
I have no intention of going through these in detail.

## Slide 11: DSEAR and RGP – Regulatory Framework (3)
Regulator - Office of Nuclear Regulation (ONR)
Licence Conditions
Permission required at some level for all activities
Contrast to other sectors
Mixture of notification and licensing (permission)
Consequence
RGP may require more explanation and justification
Notes: Suffice to say these License Conditions and the associated powers means the nuclear industry has to seek permission from the Regulator at some level for all activities.
This is in contrast to other sectors where the HSE:
applies licensing and permission regimes to certain industry sectors for specific work activities involving significant hazard, risk or public concern, for example where there are risks of:
  multiple fatalities.
  widespread and significant effects on human health.
So if the ONR is to give permission it needs to be well informed by the licensee.
Thus, the evidence and reasoning to gain permission inevitably has to be even more robust than might be expected in broader industry.
The practical outcome is that we have to approach DSEAR issues slightly differently to other industries. RGP from wider industry may require more explanation and justification than first meets the eye.

## Slide 12: DSEAR and RGP – Tolerability of Risk (1)
Is Nuclear different? Risk criteria broadly the same
=
Notes: The other aspect to discuss is the Tolerability of Risk
We’ve already seen that the regulatory regime creates greater scrutiny and consequently higher expectations on standards for nuclear operations.
But should this be the case with our non nuclear hazards?
Some suggest that “dead is dead” What kills you is irrelevant whether it be radiation or something else. This is a rationalist approach.
However, society’s tolerance to particular hazards is not necessariy rational. This involves psychology. “Nuclear” has a cultural resonance built during the Cold War. It engenders fear and dread and so society will only accept a lower risk. Fukushima causes significant harm to people due to STRESS.
The above may lead to different risk criteria for Nuclear and Non-nuclear in the future. The advantage of this would be to align us with the other high hazard industries (who are more numerous) and therefore learning (and hence Relevant Good Practice) become easier to translate.

## Slide 13: DSEAR and RGP – Tolerability of Risk (2)
Notes: Intolerable the red zone on the risk carrot. Qualitative risk assessment is usually adequate to identify if a hazard is in this region. Risks identified as “intolerable” must be mitigated regardless of cost.
To be in the Intolerable zone the risk to a worker, who has a degree of choice the risk must be 10-3 or greater And for a member of the public risks greater than 10-4 from any workplace activity are Intolerable
Broadly acceptable -. R2P2 proposes that the residual risk to an average member of the public or a worker should be of the order of 10-6 or less. Less than this threshold is Broadly Acceptable the green zone on the risk carrot
If we demonstrate the frequencies are low enough when applying RGP (i.e. standards etc.), then risks can be regarded as insignificant and adequately controlled. They are Broadly Acceptable. The Broadly Acceptable zone does not preclude using additional measures to reduce the residual risk providing that they are not grossly disproportionate in terms of time, cost and implementation difficulty for the reduction in risk achieved. At this point qualitative assessment methods apply.
The boundary between Intolerable and Broadly Acceptable is the Tolerable if ALARP. Risks here should be reduced wherever possible providing they are not grossly disproportionate.
Both qualitative and quantitative methods are needed to be able to demonstrate that the solution is ALARP. This may include a Cost-Benefit Analysis (CBA) as part of the ALARP demonstration. Any CBA should be considered persuasive not definitive. As the risk reduces the test of gross disproportionation becomes more relevant.

## Slide 14: DSEAR and RGP – Tolerability of Risk (3)
Notes: That’s R2P2 but the HSE in 1992 published the Tolerability of Risk from Nuclear Power Stations (HSE 1992).
The philosophy developed in that paper can be summarized as:
the risks to worker should be at least an order of magnitude less than the risks to workers in other industries. The suggested maximum tolerable risk to worker in any industry is 10-3; therefore, the risk to the average radiation worker facility should be less than 10-4.
Residual risks to average members of the public should be of the order of 10-6 or less from any work activity, (R2P2). Therefore, overall risk to the average member of the UK public should be less than 10-7, this is similar to the risk of being killed by lightning (R2P2).

## Slide 15: DSEAR and RGP – Tolerability of Risk (4)
Summary
Regulatory Regime
  Site Licence
  Permissioning for virtually all activities
  Robust information to regulator
Tolerability of Risk
  Residual risks targets order of magnitude less than other industries
Underpinning challenge
  Is RGP robust and effective enough
Notes: In summary:
the regulatory framework with the licence and permissioning means greater regulatory scrutiny than might otherwise be expected
the order of magnitude lower tolerability of residual
together drive a need for greater robustness to the evidence and underpinning than might be expected for other industries.
Hence why we went the further mile to answer the question: whether other industry sector practices can deliver an adequately robust underpinning.

## Slide 16: DSEAR and RGP – The Problem (1)
Unique hazard - radiolysis
Notes: We’ve set the scene so what is the hazard?
It is one that is unique to the nuclear industry.
It’s the generation of hydrogen created by radiolysis.
Radiolysis is when radiation, whether it be alpha, beta or to a lesser extent gamma, causes compounds to degrade into smaller molecular compounds or constituent elements.
When moisture is present hydrogen is formed.
Theoretically, the process can produce a stoichiometric mixture of hydrogen and oxygen. However, the actual chemistry is complex and dependent on circumstances and time. Often this means the oxygen does not manifest as gaseous oxygen, whilst the hydrogen is still released as a gas.
PVC when it undergoes radiolysis degrades to produce chlorine and hydrogen chloride, Again, the chemistry is complex.
These radiolytic processes are slow; they are dependent on the energy of the radiation, the isotopic compositions of materials, the quantities of materials and the chemical and physical circumstances.
Materials with a radiation field when stored for a long time can have an ingrowth of hydrogen and other species which can accumulate in the containment system.

## Slide 17: DSEAR and RGP – The Problem (2)
The Plant
Discrete containers
Storage array
Aggregate hydrogen - “a lot”
Individual ullage volumes about a litre
Demonstrate
  judgement robust
  residual risk acceptable
Notes: The specific problem concerns discrete containers of nuclear materials in long term storage.
They’ve been stored in a controlled environment over many years.
They are to be moved to an alternative facility as part of high hazard risk reduction operations.
Over time there may be changes to the integrity of the container.
The storage arrangement for thee containers is not unlike an insect house. It is an array of horizontal concrete tubes; sealed at one end, with access controlled at the other by a loose fitting cover.
The aggregated hydrogen is potentially “a lot” which is the best I am allowed to say.
The storage containers have an interstitial and ullage volume of about 1 litre each.
These containers are essentially sealed.
Any accumulated hydrogen will cause pressurization which can show up as bowed end caps
Basic engineering judgement says: the release of these quantities of hydrogen from a single container should not cause harm to workers.
And our problem is to underpin that judgement and show the residual risk to be acceptable

## Slide 18: DSEAR and RGP – Confirmation Bias
How to avoid?
Assume opposite is true
Variety of RGP
Consultation (avoid silo working)
Learning
Positive challenge
Group think – be aware
Downside - accusations
“mountain from a molehill”
“delay programme”
“nuclear safety case deals with it” (doesn’t it?)
Notes: The problem with any engineering judgement that’s OK is that everyone wants it to be right!
The result you have rampant confirmation bias
The approach we took to avoid this was:
First to assume the opposite is true. (In other words assume that there is a problem and it has the potential to cause harm) and proceed to assess the situation accordingly.
Use a variety of RGP techniques to address the question from different perspectives.
Use independent subject matter experts and peers to review, comment and challenge (in other words don’t work in a silo).
Seek out and use both internal and external learning.
Encourage positive but challenging behaviours demonstrated by leadership.
To be aware of group think behaviours and provide measures to identify and avoid.
The downside is being accused of:
making a “mountain out of a molehill,”
delaying the programme
it’s unnecessary because the nuclear safety case addresses the problem.
The first two require patience to explain.
The third, the interaction with the nuclear safety case, I shall come to in a moment.

## Slide 19: DSEAR and RGP – Nuclear and Non Nuclear
Six Explosion Consequences
Barometric ears, eyes, lungs, gut, loose bits
Thermal burns
Missile shrapnel injuries
Translational broken bones, penetrating wounds
Toxic acute and chronic poisoning, dose, contamination
Social & Environmental release of contaminants to environment
  Nuclear Safety Case addresses 5 & 6 NOT 1 - 4
  Fire Risk Assessment addresses 2 NOT 1, 3 & 4
Notes: A useful way to show why the nuclear doesn’t provide the justification is to look at the six types of explosion harm
1)
Barometric
the human body is not tolerant to rapid pressure changes. The result is potential damage to ears, eyes, lungs, gastrointestinal tract and certain extremities.
2)
Thermal
this is the obvious burn potential.
3)
Missile
shrapnel injuries from debris created by brittle failures due to the deflagration or detonation.
4)
Translational
expanding pressure waves and the fast moving gas can propel people over and upon landing they can incur broken bones, penetrating wounds and other blunt force traumas.
5)
Toxic
explosions can produce or release materials that can cause acute and or chronic health issues. This includes the release of radioactive materials with an associated radiation dose and contamination.
6)
Societal and Environmental Effects
These are the wider consequences beyond the site boundary that have acute and or chronic effects that impact both the general public and the environment. This includes the release of nuclear materials to the environment.
The nuclear safety case looks at specific nuclear consequences such as:
dose uptake to the public and workers
loss of containment and release of nuclear materials into the environment.
Hence it is only addressing the Toxic consequences and the Societal and Environmental consequences which it does very effectively.
However, it poorly addresses the immediate physical harm to workers or the public. This must be covered through a DSEAR risk assessment.
Fire risk assessments are often limited to thermal harm from the consequential fire
So, there’s a potential gap.
We still need that DSEAR Risk Assessment and look into the potential harm in terms of Items 1, 2, 3 and 4 to understand the potential consequences. to workers and to show that the risks are reduced to as low as is reasonably practicable,
OK when it comes to the management of dangerous substances” there is a mismatch between the scope of any nuclear safety case and the non-nuclear consequences
This has to be addressed through the DSEAR risk assessment process.

## Slide 20: DSEAR and RGP – Source Terms
Paucity of data
Hydrogen difficult to predict
Radiolysis reactant limited
Evolution rates not linear
Oxygen absorption
Limited plant inspection data
Bayesian type logic for sensitivity
Notes: To be able to assess of consequences, area classification and overall risk assessment We needed information about the quantities of hydrogen present, the pressure and the integrity of the containers etc
Unfortunately, this information was not easily available. The problem being that:
It’s exceedingly difficult to predict the hydrogen content at any moment in time because of uncertainties in the information about the moisture content of the containers.
There is PVC present and the chlorine and hydrogen chloride could’ve affected the container integrity
Radiolysis will only generate hydrogen whilst there is moisture or organic contaminants present.
The evolution rate is initially linear but changes with time. Decreasing as reactant is depleted.
Over time the oxygen is absorbed by the materials in the container resulting in the internal atmosphere becoming oxygen deficient to below the Limiting Oxygen Concentration (LOC).
We had routine inspection data for the first two decades of operation that told us that only 2% to 3% of the containers showed any deformation, the visual indication of pressurization. Unfortunately, the inspection regime was rationalized to reduce the dose detriment to the operators. This is probably an overestimate because if the deformation is plastic and the pressure is relieved through a fissure or other flow path the container will remain distorted and look as though it is still pressurized
We had no definitive data on how many containers could have become pressurized in the latter two decades.
However, one solution is to is to apply Bayesian type logic way to deduce an upper bound value purely for sensitivity analysis). This approach is purely statistical. It is not underpinned through technical knowledge of pressurization mechanisms and measurements.
This approach provides a basis for a reasoned sensitivity analysis in the consequence and risk assessments

## Slide 21: DSEAR and RGP – Range of Approaches
Four basic methodologies
The British standard BS EN 60079-10-1:2021.
The Energy Institute’s (EI) A Risk based approach to hazardous area classification.
Zone Extent by gas dispersion analysis.
Harm to individuals
  TNT energy equivalence
  Merrifield.
Notes: We now have source terms how do we use them?
The methodologies we explored were:
The British standard BS EN 60079-10-1:2021.
The Energy Institute’s (EI) A Risk based approach to hazardous area classification. (Energy Institute 1998 and Energy Institute 2015).
Gas dispersion analysis to indicate the possible extent of any area classification.
An examination of harm to individuals using TNT energy equivalence (Crowl 2003 and Merrifield 1993).
Let’s look at each in turn.

## Slide 22: DSEAR and RGP – BS EN 60079-10-1:2021 (1)
Notes: BS EN 60079-10-1:2021 is the basic go to standard when first considering area classification.
You may recognize the standard table from the BS relating ventilation ad release to an area classification.
I’m not going through the table except that if we understand the ventilation arrangements and the mechanisms of release, we can look up the area classification. Easy right?
If we take the concrete storage tubes are not ventilated. There are variable induced chimney effects. Applying the methodology in BS EN 60079-10-1 and summarized in Table 1 leads to the conclusions that:
The effectiveness of the ventilation (dilution) is Low.
Any release is not intentional; it will arise as a reasonably foreseeable fault not normal operation. The release is Secondary Grade
Therefore, the area classification indicated in Table 1 is Zone 1 possibly Zone 0.
The room housing the storage tubes and allows access to the storage tubes can be treated in the same manner.
However, the room ventilation is a cascaded reduced pressure system with low local velocities typical of nuclear installations (i.e. << 0.5 m/s) applying the detail of BS EN 60079 leads to a Low dilution.
It is a mechanical ventilation to a nuclear standard and hence the availability is more than Good
Conclusion is that the access area should be Zone 1 or even Zone 0
Each conclusion requires mandatory ignition source management and each conclusion suggests the original engineering judgment is erroneous.

## Slide 23: DSEAR and RGP – BS EN 60079-10-1:2021 (2)
Summary – Hazardous Classification and Zones
  Mandatory ignition source management
Area Classification
  Fundamentally simple probabilistic
  Emphasis on Ventilation mixing
Assessments
  Good for dense gas dispersion
  Conservative for buoyant gas dispersion
Notes: The engineering judgement took account of the potential volume of release and the coincident factors needed to get a release and achieve a flammable configuration concluding that there was little if any residual risk in the circumstances and the quantities involved.
However, the BS Area classification led to Hazardous and Zoned locations along with mandatory ignition source management.
This suggests our engineering judgement is optimistic.
The limitations of the BS include
Area classification is fundamentally a simple probabilistic methodology. It uses probability of release and probability of creating a flammable atmosphere
It is heavily dependent upon the effectiveness and availability of ventilation.
the BS EN methodology places great emphasis on the ventilation mixing and diluting releases.
Methodology is intended to cover a wide range of flammable gases predominantly dense gases and vapours.
Hydrogen is extremely buoyant, highly mobile and its own motion can generate significant mixing. This is not addressed in the methodology
These limitations make the BS EN methodology pessimistic.
Suggesting our judgement may not be as optimistic as the zoning might suggest

## Slide 24: DSEAR and RGP – Energy Institute (EI 15)
A risk based approach to hazardous area classification
Occupancy
  not always an independent variable
Vulnerability of people
Number of release sources in range
Individual risk
Flammable release probability
Ignition probability
Notes: The next approach was to use the Energy Institute’s Risk based classification methodology; it provides a probabilistic risk-based approach to boundaries of Zone 2 area classification. This is more flexible and adaptable to batch operations required for remediation type tasks, such as that considered in this application.
The methodology provides good indication of the relative changes to risks for different operations rather than absolute values.
A summary of this “Risk Based Approach to hazardous area classification” (Energy Institute1998) is included in Model code of safe practice Part 15 Area classification for installations handling flammable fluids. (Energy Institute 2015), colloquially known as EI15.
The basic formula shown here is from EI15 is
where IRignited release Maximum acceptable Individual Risk due to ignited releases. Taken to be 1.0E-5/year.
Fflam Frequency of a flammable atmosphere at the Zone 2 boundary from each release source.
Pign Probability of ignition at the Zone 2 outer boundary. Ignition probabilities are determined through standard methodology within Energy Institute 2015 and Energy Institute 2006.
Pocc Occupancy: probability that the individual is within the affected distance (hazardous area). The issue of occupancy is an area of confusion. It is easy to be seduced into believing that because each manual operation takes only a few minutes that the occupancy values are small, of the order 10-5 per year; in fact, the occupancy probability is effectively one, this is because a person has to be present for the manual operation to occur, hence it is not a truly independent variable.
V Vulnerability: probability of fatality per exposure to an ignited release.
Nrange Number of release sources within range of the individual.
The Energy Institute Risk based classification methodology, although conceived for the petrochemical industry, provides a probabilistic risk-based approach to boundaries of Zone 2 area classification. This is more flexible and adaptable to batch operations required for remediation type tasks, such as that considered in this application.
The methodology provides good indication of the relative changes to risks for different operations rather than absolute values.
A summary of the “Risk Based Approach to hazardous area classification” (Energy Institute1998) is included in Model code of safe practice Part 15 Area classification for installations handling flammable fluids. (Energy Institute 2015), colloquially known as EI15. This probabilistic approach looks at the risk to an individual from a release of flammable gas.
The basic formula from EI15 is
𝐼𝑅_(𝑖𝑔𝑛𝑖𝑡𝑒𝑑 𝑟𝑒𝑙𝑒𝑎𝑠𝑒) (𝑝𝑒𝑟 𝑦𝑒𝑎𝑟)=𝐹_(𝑓𝑙𝑎𝑚 ) (𝑝𝑒𝑟 𝑟𝑒𝑙𝑒𝑎𝑠𝑒 𝑠𝑜𝑢𝑟𝑐𝑒−𝑦𝑒𝑎𝑟)×𝑃_𝑖𝑔𝑛×𝑃_𝑜𝑐𝑐×𝑉×𝑁_𝑟𝑎𝑛𝑔𝑒
where IRignited release Maximum acceptable Individual Risk due to ignited releases. Taken to be 1.0E-5/year.
Fflam Frequency of a flammable atmosphere at the Zone 2 boundary from each release source.
Pign Probability of ignition at the Zone 2 outer boundary.
Pocc Occupancy: probability that the individual is within the affected distance (hazardous area).
V Vulnerability: probability of fatality per exposure to an ignited release.
Nrange Number of release sources within range of the individual.

## Slide 25: DSEAR and RGP – Energy Institute (EI 15)
Discussion of risk based approach to area classification
Good indication of the relative changes
Risk ranges
Identified vulnerable operations
Many operations risk “broadly acceptable”
Provided focus
Notes: The paucity of plant data precludes definitive individual risk values.
What the methodology does deliver is the relative risks for each operation and hence highlighting changes in risk between operations.
Furthermore, to account for the uncertainty, a sensitivity analysis gave a range on the upper bound and lower bound and a best estimate scenario. Applying these ranges allows an individual risk range to be expressed for each operation.
The individual risk ranges developed for each operation can be compared against the “Risk Carrot” and identify the potentially problematic operations. What this does show is that whilst for many operations the individual risk range spanned the Broadly Acceptable to the TifALARP region some are more onerous and the risk ranges traverse the TifALARP to the Intolerable region based on the bands being 10-1 lower than in R2P2. This suggests that on a probabilistic basis the BS EN area classification and zoning is extremely conservative for most operations in this application. The conclusion is not definitive and depends on the frequency of release and the number of potentially pressurized containers. The basis of safety needs refinement to address the increased risks for those operations where the range crosses the boundary from the TifALARP into the Intolerable region

## Slide 26: DSEAR and RGP – Extent of Zone (1)
Gas dispersion tools to determine extent
BS EN 60079-10-1:2015 area classification but not extent
Desktop analytical tools
Slow chronic releases
  Theoretically flammable
  So small as not to be a hazard
  Zone of Negligible Extent applies
Notes: BS EN 60079-10-1:2015 generates an area classification but does not define the extent of any designated zone.
Applying desktop analytical tools that solve the continuity equations in one geometric dimension, based on the buoyant behaviour of hydrogen, swiftly enables the conclusions:
Slow chronic releases of hydrogen will disperse due to diffusion. These releases, whilst theoretically pass through the flammable envelope, involve quantities so small as not to be a hazard. These will be a zone of Negligible Extent. The definition of Negligible Extent from the BS is:
A zone of negligible extent would also imply either a negligible release rate or a negligible release quantity and considering the volume for dispersion.
Such a zone implies that an explosion, if it takes place, will have negligible consequences.
The zone NE concept can be applied irrespective of any other adjustments for risk assessment to determine equipment protection level.

## Slide 27: DSEAR and RGP – Extent of Zone (2)
Gas dispersion tools to determine extent
BS EN 60079-10-1:2015 area classification but not extent
Desktop analytical tools
Acute releases in “insect house”
  High momentum jets
  Obstructions
  Hydrogen will layer - exits though buoyant flow and diffusion
  Buoyant thermal – mixes under own motion
Notes: Acute releases in a storage rack will be relatively short duration high momentum jets. They will encounter obstructions before the momentum is spent and the hydrogen is diluted to below the LFL, the hydrogen will then rise under buoyancy and accumulate as a layer at the ceiling space of the storage tube. This will be dispersed by a combination of buoyancy and diffusion.
Once out of the tube it will rise as a buoyant thermal and mix under its own motion

## Slide 28: DSEAR and RGP – Extent of Zone (3)
Gas dispersion tools to determine extent
BS EN 60079-10-1:2015 area classification but not extent
Desktop analytical tools
Acute releases in “insect house”
  High momentum jets
  Buoyant thermal – mixes under own motion
Notes: Acute releases outside the storage rack will again be short duration high momentum jets. Should they encounter any obstruction and lose momentum they will rise due to buoyancy as a thermal and mix to less than the LFL.

## Slide 29: DSEAR and RGP – Extent of Zone (4)
Summary of Extent
Limited extent - Right “ball park” – CFD “gilding lily”
Potentially “negligible extent” tends to support the initial judgement
  treated as non-hazardous.
  negligible release rate or negligible release quantity.
  implies negligible consequences.
  Confirm through Harm analysis
BS EN 60079-10-1 conservative
Notes: In summary, the extent of any zonal arrangements is limited and potentially of negligible extent.
The negligible extent assessment can be further underpinned by an analysis of potential harm to personnel.
This discussion uses desktop analytical tools to provide an indication of the behaviour of the hydrogen upon release. Anything more sophisticated in this circumstance such as CFD may be gilding the lily without actually improving the outcome.
The conclusions drawn from this discussion are that:
Slow chronic releases of hydrogen will disperse due to diffusion. These releases, whilst theoretically pass through the flammable envelope, involve quantities so small as not to be a hazard;
Acute releases in a channel will be as relatively short duration high momentum jets. They will encounter obstructions before the momentum is spent and the hydrogen is diluted to below the LFL, the hydrogen will rise under buoyancy and accumulate as a layer in the ceiling space of the channel. This will be dispersed from the channel by a combination of buoyancy and diffusion;
Acute releases outside the channel will again be short duration high momentum jets. Should they encounter any obstruction and lose momentum they will rise due to buoyancy as a thermal and mix to less than the LFL.
The area classifications determined using BS EN 60079-10-1 are conservative and the negligible extent tends to support the initial judgement.

## Slide 30: DSEAR and RGP – Harm
Two methods
Simple TNT Energy Equivalence
  Thumbnail comparisons of harm
Merrifield Simplified Harm assessments
Notes: What is missing is an understanding of the potential harm to people from any event involving the quantities of hydrogen in the containers.
The methods to judge the degree of harm are limited.
The common approach is to use a simple TNT Energy Equivalency and use simple thumbnail harm comparisons.
This does have drawbacks
This method has limitations.
TNT detonates; applying it to a system that deflagrates is an overestimate.
TNT Equivalency is a point source methodology. Gas cloud burns are a distributed source. However when applied to small quantities of hydrogen the burn approximates to a point source. Nonetheless it is a further conservatism.
Baker Strehlow & TNO MultiEnergy are distributed source models. They are best applied to large volumes of gas. Our situation is outside their applicability range. On face value, the refinement they offer is offset by the additional complexity and uncertainty.
An alternative on actual harm is to use the Merrifield Simplified equations. This is still based on TNT equivalency.
TNT equivalency equates the energy released by a material to a mass of TNT that would release the same amount of energy. This method is a useful indicator of consequences of a hydrogen event because it enables a direct comparison with the TNT blast data.
The basic equation is: (Crowl 2003)
Where η empirical explosion efficiency, typically between 0.01 and 0.1 (dimensionless). In the absence of empirical data an assumption is needed, Using a value of 1 is extremely conservative, using 0.1 is almost cavalier, a value of 0.5 (50%) was actually used. This is conservative but judged as not onerous.
m mass of flammable gas (hydrogen) (mass)
Ec heat of combustion of gas (energy/mass)
ETNT TNT explosion energy (energy/mass) (typically 4602 kJ/kg)
What is missing is an understanding of the potential harm to people from any event involving the quantities of hydrogen in the containers.
The methods to judge the degree of harm are limited.
The common approach is to use a simple TNT Energy Equivalency and use simple thumbnail harm comparisons.
This does have drawbacks
This method has limitations.
TNT detonates; applying it to a system that deflagrates is an overestimate.
TNT Equivalency is a point source methodology. Gas cloud burns are a distributed source. However when applied to small quantities of hydrogen the burn approximates to a point source. Nonetheless it is a further conservatism.
Baker Strehlow & TNO MultiEnergy are distributed source models. They are best applied to large volumes of gas. Our situation is outside their applicability range. On face value, the refinement they offer is offset by the additional complexity and uncertainty.
An alternative on actual harm is to use the Merrifield Simplified equations. This is still based on TNT equivalency.
TNT equivalency equates the energy released by a material to a mass of TNT that would release the same amount of energy. This method is a useful indicator of consequences of a hydrogen event because it enables a direct comparison with the TNT blast data.
The basic equation is: (Crowl 2003)
"Equivalent mass of TNT" 𝑊=(𝜂𝑚𝐸_𝑐)/𝐸_𝑇𝑁𝑇
Where η empirical explosion efficiency, typically between 0.01 and 0.1 (dimensionless). In the absence of empirical data an assumption is needed, Using a value of 1 is extremely conservative, using 0.1 is almost cavalier, a value of 0.5 (50%) was actually used. This is conservative but judged as not onerous.
m mass of flammable gas (hydrogen) (mass)
Ec heat of combustion of gas (energy/mass)
ETNT TNT explosion energy (energy/mass) (typically 4602 kJ/kg)

## Slide 31: DSEAR and RGP – TNT Thumbnails
TNT Equivalent | Consequences
1 g of Explosive | Any person holding the explosive could receive serious injury
10g of Explosive | Any person close to this quantity of explosive at the time of initiation would receive very serious injuries.1% of persons at a distance of 1.5 metres away are also liable to eardrum rupture.
100g of Explosive | 50% of windows in a room likely to be blown out. 1% eardrum rupture at 3.5 m. 50% eardrum rupture at 1.5m. Persons in very close proximity (e.g. holding the explosive) almost certainly killed
500g of Explosive | Inside a 6m x 6m enclosed brick building structural collapse is most likely; considerable damage to panels between steel or reinforced concrete frames in other structures Persons very close to blast will almost certainly be killed. Persons close to blast will be seriously injured by lung and hearing damage, fragmentation effects, and from being thrown bodily. Almost all persons within the room will sustain perforated eardrums
Notes: The TNT equivalency can be interpretated using:
simple indicative tables of effects for quantities of TNT as illustrated here.
Our release volumes fell in the range 1 to 10 g TNT and the table is not very helpful if not downright misleading
The more analytical technique of Merrifield’s Simplified Calculculations of Blast Induced Injuries and Damage offers greater clarity

## Slide 32: DSEAR and RGP – Merrifield Simplified Method
Notes: Merrifield determines probability of different injury types including the standoff distance eardrum rupture. Eardrums are the most susceptible part of the human body to rapid pressure changes and hence the most applicable injury to use as a measure of harm.
Merrifield (Merrifield 1993) provides a simple methodology to determine potential injuries from an unmitigated hydrogen event based on TNT energy equivalence. However, these predictions are conservative because
they are based on detonation events not deflagration events.
Also, the buoyant nature of hydrogen means any burn will be rising away from an operator.
It is acknowledged by Merrifield that for “energetic substances” where ‘the rate of rise in pressure is slow and the duration of the explosion is relatively long’ the method “overestimates the close-in effects and underestimates the far-field effects.” However, due to the calculation pessimisms discussed above and the small quantities of hydrogen involved, the method is judged to be an appropriate basis for this assessment.
I’ve included the table here as an illustration of the results and the injuries covered but it does show that the standoff distances to avoid serious injury are relatively small.

## Slide 33: DSEAR and RGP – Harm Summary (1)
TNT Equivalence
Denotation not deflagration
Thumbnails – not pragmatic, no recognition of conservatism
Merrifield – confirms standoff distances small, low residual risk harm
    Barometric Below Threshold & low rupture probability
    Translational Mostly Safe
Notes: This is a summary of the potential for all six injury types. (This is in terms of unmitigated harm in other words it excludes consideration of other hazard reduction methods or the application of PPE).
Barometric injuries. Short standoff distance and values are very conservative. The output shows that for the operations considered serious injuries such as lung damage are highly unlikely whilst, at normal operational distances, the worst case estimate of is a 15% chance of ear drum rupture with a less than 1% chance as a best estimate. These distances are illustrated further in Table 4 below.
Translational Injury Applying the Merrifield methodology generates values for translational but in reality, translation injuries are virtually impossible because:
  not enough energy due to small masses of hydrogen.
  an operator cannot get close enough for translational effects.
Again, the results are illustrated in Table 4 below.
Missile injury: Using standard physics and methods these effects can be estimated leading to a conclusion that:
  Containers fail in a ductile manner so low probability of generating shrapnel. Development work that pressure tested containers supports this conclusion.
  The possibility of creating other missiles is small.
  The risk of injury is low.
  The risk of missile damage to other systems is low.
Therefore, the possibility of generating missiles that can cause injury or damaged is judged to be sufficiently low that any more detailed analyses are not proportionate.
Thermal Injury: Hydrogen flames have a low thermal emissivity. An operator would have to be in close proximity to sustain any thermal injury however, even at close proximity, due to the short flame duration, it is unlikely that a thermal injury would result (Ingram 2018). The practicalities of undertaking the work mean that there is a low probability of thermal injury to an operator.
Toxic Injury: Hydrogen burns to form water. Therefore, there is no potential for direct toxic injury. The potential for breaching container integrity and losing containment of the contents is assessed in the Nuclear Safety Case.
Societal and Environmental Injury This concerns the societal effects and does not fall within the realm of DSEAR. It is better addressed by the nuclear safety case or a COMAH case. COMAH is not applicable to facilities handling nuclear materials in this instance it is an exempt nuclear facility. COMAH would normally consider the catastrophic effects, assets damage and domino effects. These are issues with wider societal impacts are addressed within the through the Nuclear Safety Case.
The assessment of the six injury types, the standoff distances illustrated in Table 3 for the hydrogen quantities of interest in these operations and the discussion on conservatism with this methodology enabled the practical conclusion that anyone at about arm’s length from the source will have a low probability of sustaining any injury.
This provided a good point from which to consider and apply the hazard hierarchy of controls to further reduce the hazard to ALARP levels, which needed to be balanced against high hazard reduction drivers. In this application some of the mitigations considered were as follows; low oxygen atmospheres, minimising occupancy of operators, maximising distance from hydrogen source to operators, keeping covers in place whenever possible, PPE (such as aprons, gloves & ear defenders), application of new containment layer as soon as possible, anti-static tools and clothing, minimising ignition sources where practicable and physical barriers to minimise direct exposure to any explosion.

## Slide 34: DSEAR and RGP – Harm Summary (2)
Other Effects
Thermal Limited due low emissivity and distance
Missile Ductile failures, most faults unconfined
Toxic
Societal and Environmental
Support original judgment
Notes: Looking at the other harm effects
Missile injury: Using standard physics and methods these effects can be estimated leading to a conclusion that:
  Containers fail in a ductile manner so low probability of generating shrapnel. Development work that pressure tested containers supports this conclusion.
  The possibility of creating other missiles is small.
  The risk of injury is low.
  The risk of missile damage to other systems is low.
Therefore, the possibility of generating missiles that can cause injury or damaged is judged to be sufficiently low that any more detailed analyses are not proportionate.
Thermal Injury: Hydrogen flames have a low thermal emissivity. The practicalities of undertaking the work mean that there is a low probability of thermal injury to an operator.
Toxic Injury: Hydrogen burns to form water. Therefore, no potential for direct toxic injury.
Societal and Environmental Injury These issues are addressed through the Nuclear Safety Case.
The understanding of harm allowed operations to be adjusted to account for standoff
In general, it supports the original judgement

## Slide 35: DSEAR and RGP – Discussion (1)
Original question – RGP underpinning of engineering judgment
BS EN 60079-10-1
  Conservative
  Drives ignition source management
  Suggest original judgement optimistic
Short dispersion distances
  Negligible extent
  Supports original judgement
Notes: The question posed was whether the engineering judgement that the hydrogen hazard associated with a facility could be underpinned using common methodologies and practices regarded as relevant good practice in other sectors. This had to meet the robustness required for the regulatory framework of the nuclear industry and meet Tolerability of Risk criteria. Overall, there was the need to avoid confirmation bias and address uncertainties in the source term information.
Applying BS EN 60079-10-1:2021 generated a conservative area classification. This methodology is driven by ventilation considerations that are better suited to dense gas and vapour dispersion and takes no account of buoyancy driven flow associated with hydrogen.
Examining the mixing distances for high velocity jets and buoyancy driven flow to define the extent of any area classification leads a conclusion that the extents were small and, in many operational situations, of negligible extent.
This suggests that the initial area classification is conservative and the original judgement more appropriate.
The use of the Energy Institute probabilistic area classification methodologies:
  Whilst not providing absolute answers is a good indicator of relative risk changes between operations.
  Allowed realistic probabilities of a hydrogen release and the potential for pressurised containers to be factored in whilst still applying a sensitivity analysis to address the paucity of data.
  changes and provides risk ranges to indicate regions of Tolerability of Risk.
  Proved effective at looking at the series of discrete operations in the process.
  Highlighted operations with increased individual risk.
  The methodology addressed the questions of occupancy and pressurised releases well.
  Allowed sensitivity to be explored.
On prima facia examination the risk ranges for some operations cross the boundary between TifALARP into the intolerable region suggesting that the original engineering judgement was inappropriate. However, what this did achieve was a focusing effort to manage the operations at greatest risk rather than have a blanket approach that would have been the case using BS EN 60079 alone.
It proved useful in highlighting relative changes in risk between discrete operations. It did not provide definitive conclusions applied with the paucity of data available.
The assessed harm potential to operators using TNT equivalency and the Merrifield 1993 methods, whilst extremely conservative (being based on detonation data rather than buoyant deflagrations) shows that the risk of any unmitigated potential harm to individuals is low and the standoff distances are small (at about arm’s length). This provided, along with the individual risks calculated, the basis to identify pragmatic ALARP mitigation measures, which need to balance the high hazard reduction drivers.

## Slide 36: DSEAR and RGP – Discussion (2)
Original question – RGP underpinning of engineering judgment
Energy Institute Risk based approach
  No absolutes
  Relative risk changes
  Good for discrete sequential operations
  Useful sensitivity
  Provided focus whereas BS EN gave a blanket view
Supports original judgement for some but not all operations
Notes: The use of the Energy Institute probabilistic area classification methodologies:
Whilst not providing absolute answers is a good indicator of relative risk changes between operations.
Allowed realistic probabilities of a hydrogen release and the potential for pressurised containers to be factored in whilst still applying a sensitivity analysis to address the paucity of data.
changes and provides risk ranges to indicate regions of Tolerability of Risk.
Proved effective at looking at the series of discrete operations in the process.
Highlighted operations with increased individual risk.
The methodology addressed the questions of occupancy and pressurised releases well.
Allowed sensitivity to be explored.
Supports the original judgement for most but not all operations

## Slide 37: DSEAR and RGP – Discussion (3)
Original question – RGP underpinning of engineering judgment
Harm discussed before
Supports original judgement for some but not all operations
Notes: We have discussed harm
In general it supported the original judgement
The assessed harm potential to operators using TNT equivalency and the Merrifield 1993 methods, whilst extremely conservative (being based on detonation data rather than buoyant deflagrations) shows that the risk of any unmitigated potential harm to individuals is low and the standoff distances are small (at about arm’s length). This provided, along with the individual risks calculated, the basis to identify pragmatic ALARP mitigation measures, which need to balance the high hazard reduction drivers.

## Slide 38: DSEAR and RGP – Conclusion
Original question – RGP underpinning of engineering judgment
Individually RGP conflicted
Engineering Judgement not right but not wrong
Transferring RGP practices focused efforts
More reasonable and logical solutions
Overall
Pragmatic & robust underpinning to engineering judgement
Notes: The overall conclusion being that individually RGP practices and methodologies from other sectors can provide conflicting evidence. When considered together they may provide challenge to each other that enables focus on those areas where the residual risk is higher and needs greater attention and avoid being ultra-conservative and preventing disproportionate attention to operations where the residual risk is small.
Overall, they did provide pragmatic and robust underpinning to the engineering judgement and highlighted the detail that engineering judgement could not cover.
We’ve had informal feedback from ONR since the writing of the paper that our approach can be considered as RGP

## Slide 39
Notes: I’ve tried to provide the Company perspective on DSEAR and our programme to improve out management of dangerous substances from a compliance perspective.
Hopefully, this puts some of the lines of enquiry into the context of SL endeavours and MSSS in particular.
On that note – have you any questions
The floor is yours