## Slide 1
HAZARDS 32
HAZ32_059
Risk Assessment Matrices – Fit For Purpose?
Tomm Childs CEng, MIChemE
Senior Process Safety Engineer, TGE Gas Engineering GmbH
www.tge-gas.com

## Slide 2: What We Do
Terminals, Storage & Distribution for Cryogenic Liquified Gases
Cryogenic storage for import, export, buffer or distribution
Import / export terminals
Liquefaction plants
Tank sizes up to 250,000 m³
All relevant infrastructure like ship, truck, container loading / unloading
Cryogenic Liquified Gases Design Experts
Plant design solutions with a high level of standardization
Fast-track & cost-effective delivery
Suitable for remote locations
Plant Conversion & Optimisation
Product change services
Activities to increase capacity
Debottlenecking
In-tank pump modernization
Creation of new revenue streams
Process Safety Assurance
All facilities are designed to International Standards
HAZOP, LOPA assurance
ATEX electrical equipment
Active and Passive Fire Protection
Emission minimisation
Notes: I’ll start with a brief introduction about TGE Gas Engineering. We are an EPC contractor that specialise in the design and build of storage and distribution terminals for Cryogenic liquids. This typically means LNG and LPG, but more recently we have seen an increasing interest in our liquified ammonia capabilities.
We also offer plant conversion and optimisation, and Process Safety Assurance, again with our expertise being in cryogenic liquefied gases.
We have a UK office in Manchester with our head office being in Bonn, Germany.

## Slide 3: Our Customers
Notes: Some of our customers, old and existing

## Slide 4: Introduction
Is the Risk Assessment Matrix “Fit For Purpose”?
Allows a quick risk assessment of a scenario
Can assess a number of scenarios and then rank them
  Prioritisation of resource (time, money)
Notes: The question I’m going to try and give my answer for – based on my experience of using Risk Assessment Matrices
First of all, for completeness and so we have a common understanding, this is what I mean by a Risk Assessment Matrix and the main benefits
I make no claim that this is a good risk assessment, it is just an example that I’ll use to illustrate some of my points

## Slide 5: Introduction
Is the Risk Assessment Matrix “Fit For Purpose”?
Risk Assessment Matrix is only a tool – so dependent on the people using it:
  What is their background (e.g. operational, engineering) and experience (e.g apprentice, 50 years in the industry)
  How in depth is their knowledge of industrial incidents (internal and external)
My answer is…
YES*
* but
Notes: Worth remembering that it is only a tool, and like any tool, its success is dependent on the experiences, capability and biases of the people using it – I think these are things that can be accounted for and can make Risk Assessments using the Risk Assessment Matrix valuable.
So, my answer…..

## Slide 6: Introduction
It can only be considered “Fit for Purpose” if:
It is used consistently for a given application
The results are repeatable
The output is used appropriately
To increase the probably of this:
It is constructed appropriately
It is used correctly and in the appropriate scenarios
It is captured in a procedure to improve consistency of its use
Notes: I think the idea of consistency and repeatability are key, we need to make the process as clear and as simple as possible, so that if two people assess the same scenario, they will come up with the same result.
How do we do that…

## Slide 7: Constructing the Risk Assessment Matrix
The Risk Assessment Matrix needs to be constructed so that it:
Fits the processes in which it is going to be used
Reflects the organisation that is going to use it
Promotes consistency in its use
The following need to be carefully considered:
Use of appropriate word models
Granularity of the Risk Assessment Matrix
Ownership and calibration
Notes: Process – e.g. management of change, HAZOP, site risk register
Origanistaion’s risk tolerance

## Slide 8: Appropriate Word Models
Consider less subjective word models, for example “heard of in industry” rather than “unlikely”
  Aids repeatability and hence consistency
Ensure word models are appropriate for the location and organisation
  “happened at the location” “happens multiple times per year in organisation” – only appropriate if the “location” is one of a number of “locations” within the wider “organisation”
  “happened at location” is not appropriate for greenfield site
Combining detailed and simplified word models with a frequency band (e.g. “heard of in industry / unlikely / 10-4 to 10-5 per year”) may provide the most consistency but does create the potential for conflict

## Slide 9: Granularity of Risk Assessment Matrix
Granularity is how detailed the Risk Assessment Matrix is:
What are the ranges of severity and frequency
How big are the divisions of severity and frequency
The granularity should be appropriate for the situations in which the Risk Assessment Matrix is going to be used:
Is having multiple divisions of the highest severity appropriate?
Is 4 orders of magnitude appropriate?
How likely is a “single” fatality vs 2 or 3
Notes: Ranges – severity should start at no effect, but where does it stop
Divisions – frequency how many orders of magnitude should each box represent
Severity - If you’re using the Risk Assessment Matrix to decide whether further assessment is required, may not be worthwhile separating these two severities, extra rows could cause confusion
Lilelihood – if the divisions are too large, all of the scenarios could end up in the same box, so not possible to use the output for prioritisation
A further point – I have single fatality on this Rik Assessment Matrix, is that really credible, people on site, in a lot of cases are usually working in groups, so would 1 to 3 fatalities be more appropriate for this row?

## Slide 10: Ownership and calibration
The Risk Assessment Matrix should be tailored to the requirements of the organisation that owns and uses it:
Calibrated to meet legal requirements, e.g. tolerability criteria inline with UK HSE expectations
Reflect the organisation’s tolerance to risk
  An organisation may deem a particular consequence/likelihood pair less tolerable and would therefore be willing to commit more resource to mitigate against it
Organisation A
Organisation B
ALARP Region
Intolerable – further measures required
Notes: As an example, organisation A deem a risk in this box to be in the ALARP region,
Oorganisation B are less tolerant to risk, on their RAM the same severity, likelihood pair is Intolerable, meaning further measures are required

## Slide 11: Use of the Risk Assessment Matrix
The following are important factors to consider when using the Risk Assessment Matrix:
Correctly defining the scenario to be assessed
Comparison of the scenario with the word models
Worst case vs most likely consequences
Taking credit for safeguards
Utilising the output appropriately
Notes: Having constructed the Risk Assessment, how it is used needs to be considered

## Slide 12: Defining the scenario to be assessed
A common issue with the use of Risk Assessment Matrices is a lack of clarity in the scenario that is being considered.
The scenario to be assessed should be fully defined and the consequence category assigned before determining the frequency
Does the orientation of the Risk Assessment Matrix influence this?
  Frequency on the x axis means this gets considered before the consequences
Notes: In my experience this is people getting mixed up between the worst case and most likely consequences
It is important to fully define the scenario and the consequences before trying to determine how frequency the event is
I’ve often thought whether the orientation makes this more likely

## Slide 13: Worst case vs most likely consequences
It is important to consider the worst case consequences of a scenario
In most cases this will be the lowest frequency outcome
By not considering the lower severity but higher frequency outcomes – the highest risk outcome may be missed
Notes: By focusing on the worst case scenario, the fact that further measures are required for the most likely outcome may be missed.

## Slide 14: Comparison of the scenario with the word model
When determining the likelihood by comparison with the word model, e.g. “heard of in industry”, care needs to be taken over what is being compared.
Do the scenarios being compared involve:
The same consequence (e.g. tank overfill vs tank overfill resulting in an explosion)
Materials with similar hazardous properties
Similar process conditions
Equipment with similar failure modes
The “heard of in industry” scenario will also have been subject to some safeguards - are these equivalent to the safeguards in the scenario being considered.

## Slide 15: Taking credit for safeguards
Dependent on the situation in which the risk assessment is being used – it may be necessary to consider existing or proposed safeguards.
What is the effect of the safeguard being considered:
Control barrier
May reduce likelihood
Mitigation measure
May reduce severity
Notes: Control barriers – stop the top event (loss of containment) (trip system)
Mitigation measures – can reduce the consequences once the top event has happened (fire and gas)

## Slide 16: Taking credit for safeguards
When determining unmitigated risk, it may still be appropriate to consider inherent safety measures, e.g.
Vessel design pressure being higher than pump shut off pressure
No bottom penetrations in a storage tank
Should conditional modifiers be used
Maintains simplicity and conservatism by not using them
Could be included in a more detailed risk assessment (e.g. LOPA) if required

## Slide 17: Utilising the output appropriately
The output from the Risk Assessment Matrix should be used to decide on the next step in the process in which it is being used. For example, based on the assessed risk:
No further risk assessment required
Further measures should be considered
A more detailed risk assessment is required
If this output is not used appropriately then either:
The Risk Assessment completed was of limited benefit
  Implementing additional measures for a tolerable risk
Risks are being inadequately managed
  Ignoring an intolerable risk
Notes: Once the risk assessment has been completed, the results need to be used for something

## Slide 18: Recording the assessment
It is critical that the assessment is recorded:
Who was involved
Inputs
  Scenario considered
  Likelihood and consequence
  Any risk reduction considered (e.g. safeguards)
Outputs
  Risk level
  Conclusions – whether further assessment or additional measures are required
This allows for interrogation of the risk assessment rationale in the future
(e.g. after an incident)
Notes: Finally

## Slide 19: Procedures and Training
For the Risk Assessment Matrix to be an effective decision making tool, it needs to be used in the most appropriate way for any given situation.
The same Risk Assessment Matrix may be used differently depending on the process it is being used in e.g. HAZOP, Management of Change
Its use also needs to be consistent
A risk assessment for the same scenario completed by two different people may have a different outcome
Variation can be minimised by ensuring all users follow a common procedure and the same assessment basis

## Slide 20: Procedures and Training
Procedures for the use of Risk Assessment matrix should include details of the following:
Defining the scenario, e.g. worst case consequence, most likely consequence
How and when should safeguards be incorporated into the assessment
How and where the inputs and outputs should be recorded (e.g. is there a template)
Training should be given to personnel expected to undertake the procedure (initial and regular refresher training)

## Slide 21: Conclusions
Risk Assessment Matrices have a number of benefits…
Quick simple assessment allowing appropriate use of resource
…but like any tool, they have their limitations
Dependent on the people using them, their experiences and biases
The effect of these limitations can be reduced by ensuring that:
The Risk Assessment Matrix is constructed appropriately
Procedures are provided which give guidance on how the Risk Assessment Matrix should be used, in any given scenario

## Slide 22: Conclusions
If a Risk Assessment Matrix has been appropriately constructed and adequate procedures are in place to guide the user in how and when to use it, the Risk Assessment Matrix can be considered
“Fit For Purpose”

## Slide 23
Contact us
TGE Gas Engineering Mildred-Scheel-Str. 1 53175 Bonn, Germany
+49 228 604480 0
tge-service@tge-gas.com
www.tge-gas.com
Follow us
LINKEDIN
@TGE Gas Engineering
TWITTER
@TGE_Gas
YOUTUBE
@TGE Gas Engineering
Click to add text