## Slide 1: How I Became a Better Safety Engineer

## Slide 2: The Event That Changed My Thinking
Explosion risk was clearly not Broadly Acceptable
Predicted high risk areas were obvious
QRA was a root cause of the accident
A random number generator would have been better.
Hydrocarbon Processing Plant

## Slide 3
Bhopal
Buncefield
Chernobyl
Feyzin
Flixborough
Would QRA have benefited?
Fukushima
Guadalajara
Longford
Macondo
Mumbai High
Pasadena
Seveso
Texas City
3 Mile Island

## Slide 4
Knowledge Based Risk
Ignorance Based Risk
Statistics
(Frequent, representative, random and ergodic)
Measurement
What is Risk?
Prediction

## Slide 5
Knowledge | Population Statistic
Risk | 1/1,000
Doctor #1
Knowledge Based Risk (KBR)
Doctor #2
Doctor #3
Which level of knowledge is reasonably practicable?
Family History
1/10
Test Results
9/10
What is the risk the patient has disease X?

## Slide 6: Pierre-Simon Laplace “Probability is a mark of our ignorance.”

## Slide 7
Knowledge vs. Ignorance Based Risk
Pre-analysis
Realisation
Post-analysis
Ignorance Based Risk (IBR)
Knowledge Based
Risk (KBR)
Risk
QRA and risk matrices
Real risk

## Slide 8
A Real Plant?
?
IBR
KBR
Real risk
?
QRA

## Slide 9
 | Probability? | Probability?
Conjunction Fallacy
Nobel Laureate Daniel Kahneman
Seveso
Poisonous cloud affecting 100,000 people
1/1,000 – 1/1,000,000
Routine weekly shutdown drops load on turbine, which increases the steam temperature above exothermic
1 – 1/10?
IBR – the real risk
KBR

## Slide 10: The Risk Prediction Paradox: Without knowing the reasons for failure, risk can be dangerously underpredicted. But, if those reasons are understood, there is no reason for prediction.

## Slide 11: A Truism: “Accidents only happen because someone thinks the risk is low.”

## Slide 12
Risk Matrices
Low or Ignorance
Based?
High or Knowledge Based?
Notes: Gamechanger when understood

## Slide 13
The Proportionality Matrix

## Slide 14
Identify variables
Business Risk Assessment & Reliability Methods
Collect data or
make estimates
Establish independence or relationships
Produce
model
Variable #1
Variable #2
Variable #3
Variable #4
Variable #5
Variable #6
Data #1
Data #2
Data #3
Data #4
Data #5
Data #6
Model

## Slide 15
Data mining
QRA & Internet Advertising Methods
Available data
Produce
model
Variable #1
Chance Correlation #2
Chance Correlation #3
Data
Model

## Slide 16
What causes major accidents?
What does not cause major accidents?
These are critical variables but they are ignored in QRA!
Bhopal, Feyzin, Seveso, Texas City
Buncefield, Pasadena
Flixborough, Guadalajara, Macondo
Piper Alpha
Mumbai High, Longford
Equipment Categories
QRA equipment categories are chance correlations!
System Complexity
Management Systems
Operating Environment
Activities
Procedures
Human Error/Factors
= Functions!
Notes: Cf WRA

## Slide 17
Recip. Comps
Filters
Flanges
Fin Fan Exch.
Centrifugal Pump
Plate Exch.
Shell Exch.
Tube Exch.
Piping
Pig Trap
Recip. Pump
Vessels
Act. Valves
Man. Valves
Tanks
Average
95% Confidence Level Upper Bound
Lower Bound
1E-3
1E-4
1E-5
Randomness in Equipment Categories
Poisson Confidence Intervals for DNV Leak Frequency Data
Compressors
Chance Correlations

## Slide 18: ‘Risk calculation’ ‘Risk estimation’ ‘Risk expert’
Risk quantification = measurement = statistics = an average
Oxymorons
Notes: So busy - Cant see wood for trees
Without verification there are no controls

## Slide 19: Well Reasoned Argument (WRA) A qualitative demonstration, possibly supported by robust quantitative data, that proportionate, systematic and scientific processes have been used to identify and understand any foreseeable hazards, and all reasonable measures have been employed to prevent or mitigate their causes and effects.
Notes: Ignorance reduction

## Slide 20
Design Envelope of System
Capability/Scope of RRM
Reliability/Life Expectancy
Diversity
Redundancy/Common Mode Failure
Availability/Overrides
Failure to Safety
Self-Revealing Failures
Defence Failure Guidewords
Overruling/Camouflaging
Survivability in Hazard Conditions
Calibration/Set-up Error
Control/Software Error
Human Error
Decision Criteria & Feedback Loops
Secondary Risks
Deterioration/Creeping Change

## Slide 21: Risk Management: “Is it just chance alone?”

## Slide 22: The time has come for change!