## Slide 1
Lesson learned from H2-related incidents: criticality of maintenance operations
Giulia Collina
PhD Candidate
NTNU – Department of Mechanical and Industrial Engineering

## Slide 2: Contents
Background
Hydrogen undesired events database
Methodology
Statistical results and discussion
Other results and discussion
Conclusion
Future step
1
2
3
4
5
6
7

## Slide 3
Hydrogen is a promising solution to achieve the target of a zero-emission society.
It has the potential to be a key player in several sectors (transportation, industry, etc.)
Fossil fuel consumption
CO2 emissions
increase
Global warming
CO2
Background

## Slide 4
Density at NTP:
0.0883 kg/m3
Flame visibility:
scarce
Colour and odour:
none
Minimum ignition energy:
0.017 mJ
Flammability range:
4 -75 %vol
Molecule diameter:
120 pm
Lower heating value:
119.96 MJ/kg
Combustion products:
H2O, NOx
No toxicity
Background

## Slide 5
prevention measures
Critical
event
Consequences
Fault events
PREVENTION
MITIGATION
Lack of maintenance
(no prevention activities)
Maintenance errors
(initiating event)
Investigation of maintenance-related undesired events in Hydrogen databases
contribute to undesired events
Maintenance activities:
Background

## Slide 6
Knowing and understanding past accidents are fundamental to avoiding similar events in the future.
Safety reporting systems are necessary to maximize the lessons learned from H2-related undesired events.
Hydrogen accident reporting

## Slide 7
Database | Hydrogen specific | N˚of H2-related events
ARIA | No | 395
eRAMS | No | 96
FACTS | No | 481
MHIDAS | No | >9000
H2TOOLS | Yes | 221
HIAD 2.0 | Yes | 628
HIRA
Hydrogen-related Incident Reports and Analyses
Alessandro Campari et al., “Analyzing Hydrogen-Related Undesired Events: A Systematic Database for Safety Assessment,” 2023, 427, https://doi.org/10.3850/978-981-18-8071-1_P021-cd.
43 numerical and categorical features to overcome the main limitation of the previous database
325 events
H2-incidents database

## Slide 8
HIAD 2.0 and MHIDAS databases
Included:
Events that occurred in the H2 supply chain
Events that involved H2-specific technologies
Events that involved flanges, piping, compressors
Releases of pure H2 or H2 -rich mixtures
Clearly defined features, categories, and glossary
HIRA

## Slide 9
Database selection
Maintenance-related events selection
Statistical results
Understanding maintenance contribution
Lack of maintenance
Generic errors / Human errors
Methodology

## Slide 10
Human errors
Petro-HRA
(Human Reliability Analysis)
9 Performance Shaping Factors (PSFs)
Time
Threat stress
Task complexity
Experience/training
Procedures
Human-machine interface
Attitudes to safety, work, and management support
Teamwork
Physical working environment
Methodology

## Slide 11
76 events
Maintenance events over the years

## Slide 12
Maintenance can contribute to the events in different ways.
Lack of maintenance: the failure could have been avoided by more effective maintenance management.
Statistical results (1)

## Slide 13
Maintenance-related undesired events occurred along the entire value chain.
Consistent with the analysis carried out considering all type of events.
Statistical results (2)

## Slide 14
Pipelines, valves, tanks and compressors responsible for most industrial failures.
Pipelines are not designed for H2 transport.
Consistent with the previous result: transportation and distribution are the most critical.
Statistical results (3)

## Slide 15
Main undetected causes:
  Hydrogen embrittlement (HE)
  Hydrogen-induced cracking (HIC)
  Hydrogen-induced stress corrosion cracking (HISC)
  High-temperature hydrogen attack (HTHA)
Equipment designed before the publication of Technical Report ISO/TR 15916 for hydrogen-materials compatibility
Selection of adequate materials and maintenance planning
Lack of maintenance: lesson-learned

## Slide 16
Explosion and fire in Sodeguara refinery in Japan in 1992.
  Break-off of the lock ring of the channel cover of a heat exchanger due to several maintenance errors:
  repeated ratcheting  reduction of diameter of the gasket retainer
  removal of insulation
1
2
Explosion and fire in an industrial plant in USA in 2011.
  Ignition of hydrogen through the friction sparks produced by maintenance operations.
Errors in maintenance: lesson-learned

## Slide 17
Event ID | Date | PSF responsible | Application stage | Component
ID 47 | 31.12.1969 | Experience/training + procedures | Hydrogen application and utilisation | Anaerobic chamber
ID 52 | 10.04.1982 | - | Hydrogen transportation and distribution | High pressure injection pipe
ID 85 | 25.05.2007 | Human-machine interface | Hydrogen application and utilisation | Compressor
ID 117 | 28.07.2005 | Experience/training | Hydrogen transportation and distribution | Pipeline
ID 256 | 21.05.1993 | Procedure | Hydrogen transportation and distribution | Coolant pipeline
ID 299 | 04.07.2003 | Procedure | Hydrogen storage | Cylinder
ID 345 | 16.06.2003 | Teamwork | Hydrogen transportation and distribution | Pipeline
ID 475 | 01.06.2019 | Attitudes to safety, work and management support | Hydrogen transportation and distribution | Shut-off valve
ID 561 | 04.08.2019 | Procedure | Hydrogen production | Generator
ID 562 | 06.07.1985 | Procedure | Hydrogen transportation and distribution | Pump gasket
ID 673 | 28.10.1996 | Procedure | ___ | Furnace
ID 717 | 10.08.2004 | - | Hydrogen application and utilisation | Anaerobic chamber
ID 718 | 05.12.1998 | Procedure | Hydrogen application and utilisation | Furnace
ID 749 | 23.04.1987 | Task complexity | Hydrogen transportation and distribution | Valve
ID 773 | 03.08.1987 | Experience/training | Hydrogen transportation and distribution | Pipeline
ID 912 | 23.02.1989 | Procedure | Hydrogen transportation and distribution | Bolt
ID 935 | 17.01.2013 | Procedure | Hydrogen transportation and distribution | Pipeline
ID 943 | 20.09.2011 | Procedure | Hydrogen transportation and distribution | Flange
ID 988 | 24.09.2019 | Procedure | Hydrogen transportation and distribution | Flange
ID 3227B | 01.10.1981 | - | Hydrogen transportation and distribution | Joint
Procedure
Formation of explosive mixture during maintenance is the most common initiating event
ISO 19880-1:2020
adequate isolation of the equipment
Errors in maintenance: lesson-learned

## Slide 18
Event ID | Date | PSF responsible | Application stage | Component
ID 47 | 31.12.1969 | Experience/training + procedures | Hydrogen application and utilisation | Anaerobic chamber
ID 52 | 10.04.1982 | - | Hydrogen transportation and distribution | High pressure injection pipe
ID 85 | 25.05.2007 | Human-machine interface | Hydrogen application and utilisation | Compressor
ID 117 | 28.07.2005 | Experience/training | Hydrogen transportation and distribution | Pipeline
ID 256 | 21.05.1993 | Procedure | Hydrogen transportation and distribution | Coolant pipeline
ID 299 | 04.07.2003 | Procedure | Hydrogen storage | Cylinder
ID 345 | 16.06.2003 | Teamwork | Hydrogen transportation and distribution | Pipeline
ID 475 | 01.06.2019 | Attitudes to safety, work and management support | Hydrogen transportation and distribution | Shut-off valve
ID 561 | 04.08.2019 | Procedure | Hydrogen production | Generator
ID 562 | 06.07.1985 | Procedure | Hydrogen transportation and distribution | Pump gasket
ID 673 | 28.10.1996 | Procedure | ___ | Furnace
ID 717 | 10.08.2004 | - | Hydrogen application and utilisation | Anaerobic chamber
ID 718 | 05.12.1998 | Procedure | Hydrogen application and utilisation | Furnace
ID 749 | 23.04.1987 | Task complexity | Hydrogen transportation and distribution | Valve
ID 773 | 03.08.1987 | Experience/training | Hydrogen transportation and distribution | Pipeline
ID 912 | 23.02.1989 | Procedure | Hydrogen transportation and distribution | Bolt
ID 935 | 17.01.2013 | Procedure | Hydrogen transportation and distribution | Pipeline
ID 943 | 20.09.2011 | Procedure | Hydrogen transportation and distribution | Flange
ID 988 | 24.09.2019 | Procedure | Hydrogen transportation and distribution | Flange
ID 3227B | 01.10.1981 | - | Hydrogen transportation and distribution | Joint
Jet fire occurred after a leakage in a chemical plant.
Maintenance operator mistakenly replaced an alloy steel elbow with a carbon steel part in a high-pressure, high-temperature line
  failure due to HTHA
Errors in maintenance: lesson-learned

## Slide 19
The HIRA database was investigated: 76 undesired events were maintenance-related.
Transportation and distribution are the most critical stages of the hydrogen value chain. Pipelines are the most critical components.
Developing proper maintenance planning is imperative to avoid events due to lack of maintenance or proper procedure. Training for operators is also essential.
Conclusion

## Slide 20: Future step
Hydrogen in several sectors: glass production
https://h2-glass.eu/
Introducing hydrogen in a new sector brings many challenges.
  Furnace and combustion development
  Analysing possible changes in the quality of products
  Safety
Maintenance approaches: risk-based maintenance

## Slide 21: Thank you for your attention
Contact
Giulia Collina: giulia.collina@ntnu.no

## Slide 22
Explosion and fire in Sodeguara refinery in Japan in 1992.
Repeated ratcheting, leading to a reduction in the diameter of the gasket retainer which keeps the heat exchanger airtight
Incorrect replacement of the gasket retainer which contributed to hydrogen gas leak
Removal of insulation, which induced temperature difference (new hazard) that led to thermal deformation of the inner parts of the tube area and contributed to the increase of the diameter of the channel barrel,
Inadequate replacement of the internal flange set bolts, leading to their destruction, increased load on the channel cover set bolts, bending and diameter decrease in the lock ring (maintenance error)