## Slide 1: Good Practices on Effectively Managing Process Safety Issues When Replicating a Modular Mid-Scale LNG Design
  Veronica Luna, HSE Director (Process Safety)

## Slide 2: Introduction and Objectives
  Modular Mid-Scale Liquefied Natural Gas (LNG) Solutions
  One of the emerging potential solutions to meet the needs of the evolving LNG market and global demand for clean energy
  Benefits
  Decrease time to market
  Lower total installed cost (TIC)
  Faster and cheaper LNG liquefactions plants
  Staged investment while generating revenue
  Flexibility to be installed in different configurations
  Modules can be installed in different location and type of facility

## Slide 3: Introduction and Objectives
Replicate to increase total plant capacity
Modify to meet Client-specific needs
Reference design as a starting point
minimal efforts in design and procurement
compressed schedule

## Slide 4: Overview of Modular Mid-Scale LNG Solutions
  Mid-scale LNG facilities produce trains in 0.7-3.0 MTPA range
  Utilizes one of the liquefaction technologies available
  Reference design
  Typical conceptual and front-end engineering design (FEED) deliverables
  Considered minimal intial overall facility needs
  Layouts maximized modular content
  Land-based but adaptable to marine facilities
  Based on a readily available and understood feedstock ang climatic conditions

## Slide 5: Process Safety Features Incorporated in Reference Design
  Hazard identification initiated
  Safety features integral to the process design incorporated
  ISD concepts incorporation maximized
  Preventive and mitigative measures in process design incorporated
  Other risk reduction measures
  Need to be site specific
AMINE
Corrosive to skin
Toxic to environment
Personnel impact
Environmental Impact
HEAVY HC
Flammable liquid
Harmful to environment
Fire
Environmental impact
REFRIGERANT
Flammable liquid/vapor
Low temperature
Asphyxiant
Fire, VCE, BLEVE
Personnel impact
LIQUEFIED NATURAL GAS
Flammable liquid/vapor
Cryogenic temperature
Asphyxiant
Fire, VCE, BLEVE
Asset impact
Personnel impact
NATURAL GAS
Flammable vapor
Fire, VCE
HYDROGEN SULFIDE
Acute toxic gas
Personnel exposure to toxic gas

## Slide 6: Considerations During the Replication Process
To copy?
or
Not to copy?

## Slide 7: Risk Management during the Base Design Development and Replication Process
Minimum Expectations
Critical Input Data
Reference: Risk Management Process (IOGP, 2018)

## Slide 8: Considerations During the Replication Process
Minimum Process Safety Requirements
Local regulations
Applicable codes and standards
Risk Tolerability Criteria
Local regulations
Client tolerability criteria
Risk Profile
Facility type
Site environmental and meteorological conditions
Client-specific requirements
Process technologies and conditions
Plot layout and arrangement

## Slide 9: Considerations during the Replication Process
 | Minimum Process Safety Requirements | Client-specific Requirements | Environmental/ Meteorological Conditions | Process Technology/ Conditions | Plot layout / arrangement | Facility Type
F&G detection provisions |  |  |  |  |  | 
Ignition control |  |  |  |  |  | 
Passive fire and explosion protection |  |  |  |  |  | 
Cryogenic protection |  |  |  |  |  | 
Active fire protection system |  |  |  |  |  | 
Emergency Shutdown system |  |  |  |  |  | 
Relief Depressurization, and Flare system |  |  |  |  |  | 
Drainage arrangement |  |  |  |  |  | 
EER arrangement |  |  |  |  |  | 
Lifesaving/ Safety equipment |  |  |  |  |  | 
Environmental protection |  |  |  |  |  | 



























































## Slide 10: Case Studies
  Case Study 1 (Base Design): Modular Mid-Scale LNG on Jack-Up Rigs
  Case Study 2: Modular Mid-Scale LNG on Fixed Jacketed Platforms
  Case Study 3: Modular Mid-Scale LNG on Sevan Unit
  Case Study 4: Modular Mid-Scale LNG Onshore

## Slide 11: Case Study 1: Modular Mid-Scale LNG on Jack-Up Rigs
  Utilized reference project for onshore
  To be installed in three offshore jack-up rigs
  Two process rigs; one utilities rig
Location is in Gulf of Mexico
Minimum safety requirements based on local regulations and class society requirements and applicable codes and standards
Safety critical elements mostly protected by location

## Slide 12: Case Study 2: Modular Mid-Scale LNG on Fixed Jacketed Platforms
  Case 1 replicated for installation on three fixed jacketed platforms
  Two process rigs; one utilities rig
  Location is in US Gulf Coast

## Slide 13: Case Study 2: Modular Mid-Scale LNG on Fixed Jacketed Platforms
PROCESS SAFETY DRIVERS
Minimium process safety requirements
SOURCE OF CHANGES
Local regulations
Appllicable codes and standards
Client-specific requirements
Classification and certifying body requirements
Local regulations
Client tolerability criteria
Facility type
Site environmental and meteorological conditions
Plot layout and arrangement
ANY CHANGES?
Y
N
N
Y
N
N
Y
Y
Y
IMPACTED PS ACTIVITIES
HSE philosophies
Engineered risk reduction measures design and their performance requirements
Risk tolerability criteria
Risk profile
Engineered risk reduction measures design and their performance requirements
HSE philosophies
HAZID/ENVID results
HSE studies results
Engineered risk reduction measures design and their performance requirements
HSE studies results
Process technologies and conditions
Y

## Slide 14: Case Study 2: Modular Mid-Scale LNG on Fixed Jacketed Platforms
© 2023 Fluor. All Rights Reserved. Fluor is a registered service mark of Fluor Corporation.
 | Minimum Process Safety Requirements | Client-specific Requirements | Environmental/ Meteorological Conditions | Process Technology/ Conditions | Plot layout / arrangement | Facility Type
F&G detection provisions |  |  |  |  |  | 
Ignition control |  |  |  |  |  | 
Passive fire and explosion protection |  |  |  |  |  | 
Cryogenic protection |  |  |  |  |  | 
Active fire protection system |  |  |  |  |  | 
Emergency Shutdown system |  |  |  |  |  | 
Relief Depressurization, and Flare system |  |  |  |  |  | 
Drainage arrangement |  |  |  |  |  | 
EER arrangement |  |  |  |  |  | 
Lifesaving/ Safety equipment |  |  |  |  |  | 
Environmental protection |  |  |  |  |  | 



















## Slide 15: Case Study 3: Modular Mid-Scale LNG on Cylindrical Floating Unit
  Case 1 replicated for installation on a cylindrical floater
  Location is in Gulf of Mexico

## Slide 16: Case Study 3: Modular Mid-Scale LNG on Sevan Unit
PROCESS SAFETY DRIVERS
Minimium process safety requirements
SOURCE OF CHANGES
Local regulations
Appllicable codes and standards
Client-specific requirements
Classification and certifying body requirements
Local regulations
Client tolerability criteria
ANY CHANGES?
N
N
N
N
N
Y
N
Y
Y
IMPACTED PS ACTIVITIES
Risk tolerability criteria
Risk profile
HSE studies results
Engineered risk reduction measures design and their performance requirements
HAZID/ENVID results
HSE studies results
Engineered risk reduction measures design and their performance requirements
HSE studies results
Process technologies and conditions
N
Site environmental and meteorological conditions
Facility type
Plot layout and arrangement

## Slide 17: Case Study 3: Modular Mid-Scale LNG on Sevan Unit
© 2023 Fluor. All Rights Reserved. Fluor is a registered service mark of Fluor Corporation.
 | Minimum Process Safety Requirements | Client-specific Requirements | Environmental/ Meteorological Conditions | Process Technology/ Conditions | Plot layout / arrangement | Facility Type
F&G detection provisions |  |  |  |  |  | 
Ignition control |  |  |  |  |  | 
Passive fire and explosion protection |  |  |  |  |  | 
Cryogenic protection |  |  |  |  |  | 
Active fire protection system |  |  |  |  |  | 
Emergency Shutdown system |  |  |  |  |  | 
Relief Depressurization, and Flare system |  |  |  |  |  | 
Drainage arrangement |  |  |  |  |  | 
EER arrangement |  |  |  |  |  | 
Lifesaving/ Safety equipment |  |  |  |  |  | 
Environmental protection |  |  |  |  |  | 


















## Slide 18: Case Study 4: Modular Mid-Scale LNG Onshore
  Case 1 replicated for installation on an onshore facility
  Different client
  Location is in British Columbia, Canada
  Two trains to be installed in phased manner

## Slide 19: Case Study 4: Modular Mid-Scale LNG Onshore
PROCESS SAFETY DRIVERS
Minimium process safety requirements
SOURCE OF CHANGES
Local regulations
Appllicable codes and standards
Client-specific requirements
Classification and certifying body requirements
Local regulations
Client tolerability criteria
Facility type
Site environmental and meteorological conditions
Plot layout and arrangement
Process technologies and conditions
ANY CHANGES?
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
IMPACTED PS ACTIVITIES
Risk tolerability criteria
Risk profile
HSE philosophies
HAZID/ENVID results
HSE studies results
Engineered risk reduction measures design and their performance requirements

## Slide 20: Case Study 4: Modular Mid-Scale LNG Onshore
© 2023 Fluor. All Rights Reserved. Fluor is a registered service mark of Fluor Corporation.
 | Minimum Process Safety Requirements | Client-specific Requirements | Environmental/ Meteorological Conditions | Process Technology/ Conditions | Plot layout / arrangement | Facility Type
F&G detection provisions |  |  |  |  |  | 
Ignition control |  |  |  |  |  | 
Passive fire and explosion protection |  |  |  |  |  | 
Cryogenic protection |  |  |  |  |  | 
Active fire protection system |  |  |  |  |  | 
Emergency Shutdown system |  |  |  |  |  | 
Relief Depressurization, and Flare system |  |  |  |  |  | 
Drainage arrangement |  |  |  |  |  | 
EER arrangement |  |  |  |  |  | 
Lifesaving/ Safety equipment |  |  |  |  |  | 
Environmental protection |  |  |  |  |  | 





































## Slide 21: Recap and Summary
  Modular mid-scale LNG solutions translates to faster and cheaper LNG liquefaction plants
  Reference design is available and can be modified to meet project specific requirements
  Customized base design can be replicated to meet capacity expansion requirements or can be installed in different facility and location
  Process safety features in reference design is limited, hence risk reduction measures are to be made project specific

## Slide 22: Recap and Summary(Cont.)
  During replication process, gap analysis shall be undertaken at the onset focusing on the three main drivers.
  Minimum process safety requirements
  Applicable risk tolerability criteria
  Facility risk profile
  Results of gap analysis shall be used to determine which risk reduction measures can be carried over from base design
  Risk management framework + gap analysis = compliant and safe design

## Slide 23
  Send me an email at veronica.christine.balangue-luna@fluor.com
  Connect with me via Linked In by scanning the QR code
Any Questions?
© 2023 Fluor. All Rights Reserved. Fluor is a registered service mark of Fluor Corporation.